How many pieces do you need to completely describe an orbit and where the spacecraft is in the orbit? (SIX)

& :  Easy to visualize location but not orbit.

Easy to measure (radar data).

or

COEs:     Easier to visualize orbit but can’t measure values directly.

a:  semimajor axis

e:  eccentricity

constant	i:  inclination	between and    	(0˚-180˚)

Ω: right ascension of asc node	between and 	(0˚-360˚)

ω: argument of perigee	between and 	(0˚-360˚)

time →	υ:  true anomaly	between and 	(0˚-360˚)

varying

Examples: Describe spacecraft location (whiz wheel problems)

1.	i = 30˚     :   along 	2.	i = 60˚	:   Northern most point (ω & υ)

Ω=180˚   :  over equator (ω & υ)		Ω=90˚	:   at perigee (υ)

ω = 0˚     :   at descending node		ω = 90˚

υ = 180˚  :  at apogee (υ)		υ = 0˚

3.	i = 90˚     :  polar orbit (i)	4.	i = 0˚	 :  Special case (no  )

Ω=270˚   :  at descending node			 :   so replace Ω & ω.

ω = 90˚    : also at the + axis               e= 0˚ » no  so replace ω & υ

υ =  90˚                                                    i & e = 0˚ » replace 	Ω, ω, & υ

We’ll learn how to calculate COEs from  & . For now, let’s see what we can figure out by inspection.

1.	 = 7000 	2. 	 = -10,000  -10,000

= 8.5 		 = -6

- - - - - - - - - - - - - - - - -		- - - - - - - - - - - - - - - - - - - -

spacecraft over North pole	spacecraft over equator @ descending node

i = 90˚ 		i = 90˚

Ω=270˚   		Ω=45˚

S/C @ perigee  or  apogee		S/C @ perigee  or  apogee

ω = 90˚       ω = 270˚		            ω = 180˚      ω = 0˚

υ = 0˚           υ = 180˚  		             υ = 0˚          υ = 180˚

3.	 = 12,000 	4. 	 = 8,000  -8,000

= 5  - 5 		 = 7

- - - - - - - - - - - - - - - - -		- - - - - - - - - - - - - - - - - - - -

s/c over equator @ descending node	s/c over 45˚ S. latitude & headed due East

i = 135˚ (westward motion)		i = 45˚

Ω=270˚   		Ω=90˚

S/C @ perigee  or  apogee		S/C @ perigee  or  apogee

ω = 180˚       ω = 0˚		            ω = 270˚      ω = 90˚

υ = 0˚           υ = 180˚  		             υ = 0˚          υ = 180˚