## Slide 1
Back-In Angle and Perpendicular Parking

## Slide 2: What are the benefits of backing into parking spaces?
Can enter and exit easier
Takes less time to park and exit
Can see better when leaving
Prevents backing out into traffic
Better control and lowers risk

## Slide 3
Back-In Angle Parking

## Slide 4: Approach
Check front and rear
Signal right
Side Position 3
(3 feet) from the
parking space.
Reference Point- middle of the right half of the hood

## Slide 5: Reference for 3 feet

## Slide 6: Approach
Pull past the space and stop
Before backing
Shift to reverse
Check 360°

## Slide 7: Backing In
Target and back slowly
Turn the wheel when the pivot point aligns with the space

## Slide 8: Complete park
Straighten car and tires
Stop at Rear Position
Reference Point: 1 foot behind door post or middle of rear passenger window

## Slide 10: To Exit the Parking Space
Shift to drive
Check traffic
Signal
Pull out when clear

## Slide 11: Back-In Perpendicular Parking

## Slide 12: Approach
Check front and rear
Signal right
Side Position 3
(3 feet) from the
parking space.
Reference Point- middle of the right half of the hood

## Slide 13: Approach
Pull forward until your body is aligned in the center of the space
Select 45° Target – over outside edge of the driver’s side mirror

## Slide 14: Start Park
Turn wheel fully left, creep forward until on target
Turn the wheel fully to the right
Do 360° search
Reverse and back slowly until vehicle is perpendicular with the space

## Slide 15: Backing In
Turn the wheel fully to the right
Do 360° search
Reverse and back slowly until vehicle is perpendicular with the space

## Slide 16: Backing In
Continue backing until your car is on target
Stop and straighten the wheel

## Slide 17: Backing In
Continue backing and stop at Rear Position
Secure car

## Slide 18: Exiting the space
Shift to drive
Check traffic
Signal
Pull out when clear